## Slide 1: Computer Architecture Project
Performance Analysis of a Multi-thread K-Means solution
Antonio Patimo
Guillaume Quint
A.Y. 2022/23

## Slide 2: Product presentation
Scenario: International Bank wants to identify client groups based on their monthly income and expenditure to propose personalized investment plans
Typical use case: 10M users, 5 groups
Product: customer clustering software for personalized advertisement
Algorithm: parallelized K-means clustering

## Slide 3: Parallel K-Means
The main thread initializes the centroids randomly and splits the dataset between all threads, so that each of them works on its own partition
Each thread associates every point to one of the current centroids
Each thread computes the number and the sum of coordinates of the points associated to each centroid
The main thread updates the centroids based on threads’ results and continues until convergence

## Slide 4: Hardware Specifications
Intel i7-6700HQ | 
CPU cores | 4
Threads | 8
L1 cache | 4 x 32 KB 8-way set associative instruction caches 4 x 32 KB 8-way set associative data caches
L2 cache | 4 x 256 KB 4-way set associative caches
L3 cache | 6 MB 12-way set associative shared cache

## Slide 5: Conclusioni speed-up 1° soluzione (1 slide per conclusione sul perché)
Correlazione positiva tra speeed-up e carico di lavoro
  Nota su cache miss/hit
Analisi tempo di esecuzione al crescere del # di threads
Shift verso destra del picco di speedup

## Slide 6: Execution Time
Chart: Threads
100M | 6.0213 | 3.5343 | 2.9543 | 2.452 | 2.252 | 2.1417 | 1.8902 | 1.9223 | 1.8403 | 1.8841 | 1.7761 | 1.7861 | 1.7636 | 1.8264 | 1.7689 | 1.8331 | 1.7239 | 1.7177 | 1.7198 | 1.7141
10M | 2.7708 | 1.7453 | 1.4214 | 1.2468 | 1.1081 | 1.0394 | 0.93485 | 0.94269 | 1.0542 | 1.0267 | 0.98009 | 0.95415 | 0.93537 | 0.88633 | 0.88763 | 0.8721 | 0.91697 | 0.91383 | 0.9017 | 0.89914
1M | 0.060944 | 0.039546 | 0.035094 | 0.028383 | 0.027728 | 0.024337 | 0.021979 | 0.021837 | 0.025357 | 0.023974 | 0.023504 | 0.023523 | 0.022897 | 0.021866 | 0.021713 | 0.02124 | 0.022061 | 0.02152 | 0.022048 | 0.021809
100k | 0.0074532 | 0.0075758 | 0.0067338 | 0.0058677 | 0.0062044 | 0.0058242 | 0.0053791 | 0.0052075 | 0.0051325 | 0.0048392 | 0.0047351 | 0.0047127 | 0.0047606 | 0.0046679 | 0.0050873 | 0.0049784 | 0.0050839 | 0.0051026 | 0.0053072 | 0.0054337
10k | 0.00080377 | 0.0012685 | 0.0015257 | 0.0015694 | 0.0018704 | 0.0020106 | 0.002191 | 0.0025054 | 0.002899 | 0.0031248 | 0.0035767 | 0.0036928 | 0.0039748 | 0.0042114 | 0.0044699 | 0.0048857 | 0.004866 | 0.0052943 | 0.0054426 | 0.0056337

## Slide 7: Speedup
With a small dataset, increasing the number of threads reduces the speedup
With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns
With a larger dataset the speedup increases
Chart: Threads
100M | 1 | 1.7037 | 2.0382 | 2.4556 | 2.6738 | 2.8115 | 3.1855 | 3.1324 | 3.2719 | 3.1959 | 3.3901 | 3.3712 | 3.4143 | 3.2969 | 3.4041 | 3.2848 | 3.4928 | 3.5054 | 3.5012 | 3.5128
10M | 1 | 1.5876 | 1.9493 | 2.2223 | 2.5004 | 2.6658 | 2.9639 | 2.9392 | 2.6283 | 2.6987 | 2.8271 | 2.9039 | 2.9623 | 3.1261 | 3.1216 | 3.1771 | 3.0217 | 3.0321 | 3.0728 | 3.0816
1M | 1 | 1.5411 | 1.7366 | 2.1472 | 2.1979 | 2.5041 | 2.7728 | 2.7909 | 2.4035 | 2.5421 | 2.5929 | 2.5908 | 2.6616 | 2.7872 | 2.8069 | 2.8693 | 2.7626 | 2.832 | 2.7642 | 2.7944
100k | 1 | 0.98381 | 1.1068 | 1.2702 | 1.2013 | 1.2797 | 1.3856 | 1.4312 | 1.4522 | 1.5402 | 1.574 | 1.5815 | 1.5656 | 1.5967 | 1.465 | 1.4971 | 1.466 | 1.4607 | 1.4044 | 1.3716
10k | 1 | 0.63362 | 0.52682 | 0.51215 | 0.42972 | 0.39977 | 0.36684 | 0.32082 | 0.27726 | 0.25722 | 0.22472 | 0.21766 | 0.20221 | 0.19086 | 0.17982 | 0.16452 | 0.16518 | 0.15182 | 0.14768 | 0.14267

## Slide 8: With a small dataset, increasing the number of threads reduces the speedup
Using the VTune profiler, we observe that the CPU time spent waiting for thread termination goes from an average of 0,046s using 2 threads to 0,362s using 15 threads
Because the dataset is small, the total time spent by working threads in both cases is negligeable
Therefore, with an increasing overhead we see an increase in execution time and so a reduction in speedup

## Slide 9: With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns
This phenomenon happens because increasing the number of threads decreases the amount of work for threads
when the last thread begins its work, the first ones are almost done, which means that less work is done in parallel
Because of this we reach a maximum threshold of threads working in parallel

## Slide 10: With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns
Chart: CPU utilization (total program execution) with 10M points dataset
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
2 threads (avg: 1.629) | 9.421 | 6.938 | 58.947 | 0 | 0 | 0 | 0 | 0 | 0
5 threads (avg: 3,055) | 10.39 | 4.906 | 3.503 | 3.803 | 5.281 | 23.608 | 0 | 0 | 0
10 threads (avg: 2.42) | 12.825 | 9.042 | 9.448 | 10.198 | 6.928 | 5.828 | 4.218 | 0.519 | 0.001

## Slide 11: With a larger dataset the speedup increases
The sequential part of the application is almost constant w.r.t. the dataset size. Meanwhile, with a larger dataset, the work done in parallel by threads increases
#TODO inserire stacked bar chart with CPUTime/ElapsedTime (1M(?), 10M, 100M)