## Slide 1: Computer Architecture Project
Performance Analysis of a Multi-thread K-Means solution
Antonio Patimo
Guillaume Quint
A.Y. 2022/23

## Slide 2: Product presentation
Scenario: International Bank wants to identify client groups based on their monthly income and expenditure to propose personalized investment plans
Typical use case: 10M users, 5 groups
Product: customer clustering software for personalized advertisement
Algorithm: parallelized K-means clustering

## Slide 3: Parallel K-Means
The main thread initializes the centroids randomly and splits the dataset between all threads, so that each of them works on its own partition
Each thread associates every point to one of the current centroids
Each thread computes the number and the sum of coordinates of the points associated to each centroid
The main thread updates the centroids based on threads’ results and continues until convergence

## Slide 4: Hardware Specifications
Intel i7-6700HQ | 
CPU cores | 4
Threads | 8
L1 cache | 4 x 32 KB 8-way set associative instruction caches 4 x 32 KB 8-way set associative data caches
L2 cache | 4 x 256 KB 4-way set associative caches
L3 cache | 6 MB 12-way set associative shared cache

## Slide 5: Execution Time
Chart: Threads
100M | 6.0213 | 3.5343 | 2.9543 | 2.452 | 2.252 | 2.1417 | 1.8902 | 1.9223 | 1.8403 | 1.8841 | 1.7761 | 1.7861 | 1.7636 | 1.8264 | 1.7689 | 1.8331 | 1.7239 | 1.7177 | 1.7198 | 1.7141
10M | 2.7708 | 1.7453 | 1.4214 | 1.2468 | 1.1081 | 1.0394 | 0.93485 | 0.94269 | 1.0542 | 1.0267 | 0.98009 | 0.95415 | 0.93537 | 0.88633 | 0.88763 | 0.8721 | 0.91697 | 0.91383 | 0.9017 | 0.89914
1M | 0.060944 | 0.039546 | 0.035094 | 0.028383 | 0.027728 | 0.024337 | 0.021979 | 0.021837 | 0.025357 | 0.023974 | 0.023504 | 0.023523 | 0.022897 | 0.021866 | 0.021713 | 0.02124 | 0.022061 | 0.02152 | 0.022048 | 0.021809
100k | 0.0074532 | 0.0075758 | 0.0067338 | 0.0058677 | 0.0062044 | 0.0058242 | 0.0053791 | 0.0052075 | 0.0051325 | 0.0048392 | 0.0047351 | 0.0047127 | 0.0047606 | 0.0046679 | 0.0050873 | 0.0049784 | 0.0050839 | 0.0051026 | 0.0053072 | 0.0054337
10k | 0.00080377 | 0.0012685 | 0.0015257 | 0.0015694 | 0.0018704 | 0.0020106 | 0.002191 | 0.0025054 | 0.002899 | 0.0031248 | 0.0035767 | 0.0036928 | 0.0039748 | 0.0042114 | 0.0044699 | 0.0048857 | 0.004866 | 0.0052943 | 0.0054426 | 0.0056337

## Slide 6: Speedup
With a small dataset, increasing the number of threads reduces the speedup
With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns until a threshold
With a larger dataset the speedup increases
Chart: Threads
100M | 1 | 1.7037 | 2.0382 | 2.4556 | 2.6738 | 2.8115 | 3.1855 | 3.1324 | 3.2719 | 3.1959 | 3.3901 | 3.3712 | 3.4143 | 3.2969 | 3.4041 | 3.2848 | 3.4928 | 3.5054 | 3.5012 | 3.5128
10M | 1 | 1.5876 | 1.9493 | 2.2223 | 2.5004 | 2.6658 | 2.9639 | 2.9392 | 2.6283 | 2.6987 | 2.8271 | 2.9039 | 2.9623 | 3.1261 | 3.1216 | 3.1771 | 3.0217 | 3.0321 | 3.0728 | 3.0816
1M | 1 | 1.5411 | 1.7366 | 2.1472 | 2.1979 | 2.5041 | 2.7728 | 2.7909 | 2.4035 | 2.5421 | 2.5929 | 2.5908 | 2.6616 | 2.7872 | 2.8069 | 2.8693 | 2.7626 | 2.832 | 2.7642 | 2.7944
100k | 1 | 0.98381 | 1.1068 | 1.2702 | 1.2013 | 1.2797 | 1.3856 | 1.4312 | 1.4522 | 1.5402 | 1.574 | 1.5815 | 1.5656 | 1.5967 | 1.465 | 1.4971 | 1.466 | 1.4607 | 1.4044 | 1.3716
10k | 1 | 0.63362 | 0.52682 | 0.51215 | 0.42972 | 0.39977 | 0.36684 | 0.32082 | 0.27726 | 0.25722 | 0.22472 | 0.21766 | 0.20221 | 0.19086 | 0.17982 | 0.16452 | 0.16518 | 0.15182 | 0.14768 | 0.14267

## Slide 7: 1. With a small dataset, increasing the number of threads reduces the speedup
Using the VTune profiler, we observe that the CPU time spent waiting for thread termination goes from an average of 0,046s using 2 threads to 0,362s using 15 threads
Because the dataset is small, the total time spent by working threads in both cases is negligeable
Therefore, with an increasing overhead we see an increase in execution time and so a reduction in speedup

## Slide 8: 2. With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns until a threshold
With larger datasets, dividing the work among more threads is much more beneficial than the overhead introduced.
For example, considering 10M points dataset, doubling the number of threads from 8 to 16 brings an average execution time from 212ms to 137ms. Meanwhile the overhead only increases from 26ms to 49ms. Therefore the total iteration time is reduced from 239ms to 186ms.
To observe a substantial reduction in performance due to overhead, we must increase a lot the number of threads or consider much smaller datasets.

## Slide 9: 2. With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns until a threshold

## Slide 10: 2. With larger datasets, increasing the number of threads yields an improved speedup with progressively diminishing returns until a threshold

## Slide 11: 3. With a larger dataset the speedup increases
The sequential part of the application is almost constant with respect to the dataset size. Meanwhile, with a larger dataset, the work done in parallel increases
Therefore, the ratio between CPU Time and Elapsed Time increases
Chart: CPU Time / Elapsed Time (7 threads)
| 1M | 10M | 100M
Elapsed Time (seconds) | 2.553 | 44.458 | 84.734
CPU Time (seconds) | 0.157 | 146.914 | 398.041
Compression Rate | 0.061496 | 3.3046 | 4.6975

## Slide 12: Performance Optimization
Chart: Execution Time comparison (10M)
Before | 2.7708 | 1.7453 | 1.4214 | 1.2468 | 1.1081 | 1.0394 | 0.93485 | 0.94269 | 1.0542 | 1.0267 | 0.98009 | 0.95415 | 0.93537 | 0.88633 | 0.88763 | 0.8721 | 0.91697 | 0.91383 | 0.9017 | 0.89914
After | 2.6884 | 1.5443 | 1.1651 | 0.97194 | 0.96092 | 0.85506 | 0.78674 | 0.73637 | 0.8876 | 0.85614 | 0.85209 | 0.82372 | 0.79541 | 0.76924 | 0.74151 | 0.74142 | 0.81656 | 0.79377 | 0.80027 | 0.79029

## Slide 13: Performance Optimization
Chart: Speedup comparison (10M)
After | 1 | 1.7409 | 2.3075 | 2.766 | 2.7977 | 3.1441 | 3.4171 | 3.6508 | 3.0288 | 3.1401 | 3.155 | 3.2637 | 3.3799 | 3.4948 | 3.6255 | 3.626 | 3.2923 | 3.3868 | 3.3593 | 3.4017
Before | 1 | 1.5876 | 1.9493 | 2.2223 | 2.5004 | 2.6658 | 2.9639 | 2.9392 | 2.6283 | 2.6987 | 2.8271 | 2.9039 | 2.9623 | 3.1261 | 3.1216 | 3.1771 | 3.0217 | 3.0321 | 3.0728 | 3.0816

## Slide 14: Performance Optimization
Inside the worker function, we found that aggregatePoints took much more time to execute than initially expected

## Slide 15: Performance Optimization
We factored the work done by the aggregatePoints inside the threads’ worker function but we experienced a decrease in performances, mainly due to an increased in data sharing among threads.

## Slide 16: Performance Optimization
We used local data structures for each thread to store partial results in order to avoid mutual cache invalidations